## Slide 1: The KeyGlove
1

## Slide 2
A human-computer interface (HCI) is the mean of communication between a human user and a computer system.
The use of input/output devices with supporting software.
Devices of increasing sophistication are becoming available to mediate the human-computer interaction.
Human Computer Interface

## Slide 3
Hand motion tracking
Five different keys
Light and easy to wear
It can replace a mouse, a joystick or a keyboard
Different modalities are implemented
The KeyGlove

## Slide 4
x2 FIreBeetle esp32 (central and peripheral)
x5 flex sensors
Gyroscope MPU6050
PCB
x5 22kΩ resistors
x2 LEDs
x2 100Ω resistors
Hardware

## Slide 5
VIDEO DEMO

## Slide 6
Gyroscope:
Libraries “Wire.h” and “MPU6050_6Axis_MotionApps20.h” used
Euler Angles are computed
Calibration phase
I2C communication (SCL and SDA)
Interrupts enabled every time the value of an angle changes
Arduino

## Slide 7
Flex Sensors:
Voltage divider to sense the resistance change of the flex sensor
Thresholds are computed empirically
Sampling frequency 20 Hz
Analog Read:
  If raw value<threshold 🡪 Flex
  If raw value>threshold 🡪 No flex
Flex sensor
22kΩ
Arduino

## Slide 8
Gyroscope initialization phase
  Offset is computed
  Interrupt detection enabled
  The device is ready
Serial communication
  Gyroscope data (‘g’)
    Relative angle drift from starting point
  Flex sensors data (‘f’)
    1🡪Flex
    0🡪 No flex
Arduino

## Slide 9
Wrapper class of the Robot class from java.awt package
  Move mouse around and simulate mouse and key presses
Versatile
  Able to change the sensors as long as the user tells us which sensor data is which finger
Processing Backend

## Slide 10
Main backbone of the program
  Each finger is assigned a Boolean (0 for unbent, 1 for bent)
  For each event, there is comment describing how to activate the event
  (thumb, index, middle, ring, pinky)
Two Modes
  Mouse mode, able to click
  Keyboard mode, able to type
Processing Backend

## Slide 11
Keyboard option (similar to phone keypad) by flexing the finger multiple times to switch to character
  Thumb: Send character
  Index: A – F
  Middle: G – L
  Ring: M – S
  Pinky: T - Z
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
SEND
Processing Backend

## Slide 12
Processing Frontend

## Slide 13
Processing Frontend